## Slide 1: P&S Modern SSDs NAND Flash Read/Write Operations
Dr. Mohammad Sadrosadati
Prof. Onur Mutlu
ETH Zürich
Fall 2022
19 October 2022

## Slide 2: Upcoming EFCL & SAFARI Live Seminar (Oct. 19)
https://www.youtube.com/watch?v=5BRlkCCL-hY

## Slide 3: Today’s Agenda
NAND Flash Page Read/Write
Sensing Circuitry

## Slide 4: Today’s Agenda
NAND Flash Page Read/Write
Sensing Circuitry

## Slide 5: A Flash Cell
Basically, it is a transistor
S
(Source)
D
(Drain)
Substrate
G
(Control Gate)
VGS
ID
ID
VTH
(Threshold Voltage)
VGS >VTH
VGS < VTH

## Slide 6: A Flash Cell
Basically, it is a transistor
  w/ a special material: Floating gate (2D) or Charge trap (3D)
S
(Source)
D
(Drain)
Substrate
G
(Control Gate)
VGS
ID
VTH
FG
(Floating Gate)

## Slide 7: A Flash Cell
Basically, it is a transistor
  w/ a special material: Floating gate (2D) or Charge trap (3D)
  Can hold electrons in a non-volatile manner
S
(Source)
D
(Drain)
Substrate
G
(Control Gate)
VGS
ID
VTH
FG
(Floating Gate)
VPGM = 20 V
GND
–
–
–
–
Tunneling

## Slide 8: A Flash Cell
Basically, it is a transistor
  w/ a special material: Floating gate (2D) or Charge trap (3D)
  Can hold electrons in a non-volatile manner
  Changes the cell’s threshold voltage (VTH)
S
(Source)
D
(Drain)
Substrate
G
(Control Gate)
VGS
ID
VTH
FG
(Floating Gate)
VTH'
Tunneling
GND
20 V
–
–
–
–
VREF
VTH < VREF
VTH > VREF
‘1’
‘0’

## Slide 9: Threshold Voltage Distribution
VTH distribution of cells in a programmed page/block/chip
Why distribution? Variations across the cells
  Some cells are more easily programmed or erased
# of cells
Erased (E)
0
Programmed
1
VREF
Threshold voltage (VTH)
y
x
There are y cells whose VTH = x V

## Slide 10: VTH Distribution of MLC NAND Flash
Multi-level cell (MLC) technique
  2m VTH states required to store m bits in a single flash cell
Limited width of the VTH window: Need to
  Make each VTH state narrow
  Guarantee sufficient margins b/w adjacent VTH states
# of cells
111
E
110
P1
100
P2
000
P3
010
P4
011
P5
001
P6
101
P7
MSB
LSB
CSB
V
TH
margin
V
TH
V
REF0
V
REF1
V
REF2
V
REF3
V
REF4
V
REF5
V
REF6

## Slide 11: VTH Distribution of MLC NAND Flash
Multi-level cell (MLC) technique
  2m VTH states required to store m bits in a single flash cell
Limited width of the VTH window: Need to
  Make each VTH state narrow
  Guarantee sufficient margins b/w adjacent VTH states
    VTH changes over time after programmed
    Narrower margins  Lower reliability
    More bits per cell  higher density but lower reliability
# of cells
111
E
110
P1
100
P2
000
P3
010
P4
011
P5
001
P6
101
P7
MSB
LSB
CSB
V
TH
margin
V
TH
V
REF0
V
REF1
V
REF2
V
REF3
V
REF4
V
REF5
V
REF6
Shifted & widened after programmed
Error cells

## Slide 12: Basic Operation: Page Program
…
BL0
…
BL1
…
BL2
…
BL3
…
BL132,095
SSL
Wordline
WLk-1
WLk
GSL
…
…
…
…
Target Page
Block
WLk+1
…
…
…
…
…
…
String Select Line
Ground Select Line

## Slide 13: Basic Operation: Page Program
…
BL0
…
BL1
…
BL2
…
BL3
…
BL132,095
SSL
Wordline
WLk-1
WLk
GSL
…
…
…
…
WLk+1
…
…
…
…
…
…
String Select Line
Ground Select Line
WL control – All other cells operate as a resistance
VCC
VPASS
VPROG
VPASS
VCC

## Slide 14: Basic Operation: Page Program
BL control – Inhibits cells to not be programmed
BL0
BL1
BL2
BL3
BL132,095
WLk
…
VPROG
0
1
0
1
0
program
inhibit

## Slide 15: Basic Operation: Page Program
BL control – Inhibits cells to not be programmed
BL0
BL1
BL2
BL3
BL132,095
WLk
…
VPROG
0
1
0
1
0
program
inhibit
To GND
To VCC
To GND
To VCC
To GND

## Slide 16: Basic Operation: Page Program
BL0
BL1
BL2
BL3
BL132,095
WLk
…
VPROG
0
1
0
1
0
program
inhibit
To GND
To VCC
To GND
To VCC
To GND
# of cells
Erased (E)
1
VREF
Threshold voltage (VTH)

## Slide 17: Basic Operation: Page Program
BL0
BL1
BL2
BL3
BL132,095
WLk
…
VPROG
0
1
0
1
0
program
inhibit
To GND
To VCC
To GND
To VCC
To GND
# of cells
Erased (E)
0
Programmed
1
VREF
Threshold voltage (VTH)
Inhibited cells
Programmed cells

## Slide 18: Basic Operation: Page Program
BL0
BL1
BL2
BL3
BL132,095
WLk
…
VPROG
0
1
0
1
0
program
inhibit
To GND
To VCC
To GND
To VCC
To GND
# of cells
Erased (E)
1
VREF
Threshold voltage (VTH)
Inhibited cells
Cells to program
Hard-to-program cells
Easy-to-program cells

## Slide 19: Basic Operation: Page Program
Incremental Step-Pulse Programming (ISPP)
BL0
BL1
BL2
BL3
BL132,095
WLk
…
VPROG0
0
1
0
1
0
program
inhibit
To GND
To VCC
To GND
To VCC
To GND
# of cells
Erased (E)
1
VREF
Threshold voltage (VTH)
Inhibited cells
Cells to program
Verified as programmed

## Slide 20: Basic Operation: Page Program
Incremental Step-Pulse Programming (ISPP)
BL0
BL1
BL2
BL3
BL132,095
WLk
…
0
1
0
1
0
program
inhibit
To GND
To VCC
To VCC
To VCC
To GND
# of cells
Erased (E)
1
VREF
Threshold voltage (VTH)
Inhibited cells
Cells to program
Inhibit programmed cells

## Slide 21: Basic Operation: Page Program
Incremental Step-Pulse Programming (ISPP)
BL0
BL1
BL2
BL3
BL132,095
WLk
…
VPROG1
0
1
0
1
0
program
inhibit
To GND
To VCC
To VCC
To VCC
To GND
# of cells
Erased (E)
1
VREF
Threshold voltage (VTH)
Inhibited cells
Cells to program
Inhibit programmed cells

## Slide 22: Basic Operation: Page Program
Incremental Step-Pulse Programming (ISPP)
BL0
BL1
BL2
BL3
BL132,095
WLk
…
VPROG1
0
1
0
1
0
program
inhibit
To GND
To VCC
To VCC
To VCC
To GND
# of cells
Erased (E)
1
VREF
Threshold voltage (VTH)
Inhibited cells
Cells to program
Inhibit programmed cells
Programmed
0

## Slide 23: Basic Operation: Page Read
WL control – All other cells operate as a resistance
BL0
BL1
BL2
BL3
BL132,095
WLk
…
VREF
0
1
0
1
0
# of cells
Erased (E)
1
VREF
Threshold voltage (VTH)
Programmed
0

## Slide 24: Basic Operation: Page Read
BL control – Charge all BLs
BL0
BL1
BL2
BL3
BL132,095
WLk
…
VREF
0
1
0
1
0
To Vcc
To VCC
To VCC
To VCC
To VCC
# of cells
Erased (E)
1
VREF
Threshold voltage (VTH)
Programmed
0

## Slide 25: Basic Operation: Page Read
Sensing the current through BLs
BL0
BL1
BL2
BL3
BL132,095
WLk
…
VREF
0
1
0
1
0
0 (No current)
1 (Current)
0
1
0
# of cells
Erased (E)
1
VREF
Threshold voltage (VTH)
Programmed
0
VTH < VREF
VTH > VREF

## Slide 26: Basic Operation: Page Read - MLC
Sensing the current through BLs
BL0
BL1
BL2
BL3
BL132,095
WLk
…
111
000
101
001
110
# of cells
111
E
110
P1
100
P2
000
P3
010
P4
011
P5
001
P6
101
P7
MSB
LSB
CSB
V
TH
V
REF0
V
REF1
V
REF2
V
REF3
V
REF4
V
REF5
V
REF6

## Slide 27: Basic Operation: Page Read - MLC
Sensing the current through BLs
BL0
BL1
BL2
BL3
BL132,095
WLk
…
111
000
101
001
110
# of cells
111
E
110
P1
100
P2
000
P3
010
P4
011
P5
001
P6
101
P7
MSB
LSB
CSB
V
TH
V
REF0
V
REF1
V
REF2
V
REF3
V
REF4
V
REF5
V
REF6

## Slide 28: Basic Operation: Page Read - MLC
Sensing the current through BLs
BL0
BL1
BL2
BL3
BL132,095
WLk
…
111
000
101
001
110
# of cells
111
E
110
P1
100
P2
000
P3
010
P4
011
P5
001
P6
101
P7
MSB
LSB
CSB
V
TH
V
REF0
V
REF1
V
REF2
V
REF3
V
REF4
V
REF5
V
REF6

## Slide 29: Basic Operation: Page Read - MLC
Sensing the current through BLs
BL0
BL1
BL2
BL3
BL132,095
WLk
…
111
000
101
001
110
# of cells
111
E
110
P1
100
P2
000
P3
010
P4
011
P5
001
P6
101
P7
MSB
LSB
CSB
V
TH
V
REF0
V
REF1
V
REF2
V
REF3
V
REF4
V
REF5
V
REF6

## Slide 30: Basic Operation: Page Read - MLC
Sensing the current through BLs
BL0
BL1
BL2
BL3
BL132,095
WLk
…
111
101
001
110
# of cells
111
E
110
P1
100
P2
000
P3
010
P4
011
P5
001
P6
101
P7
MSB
LSB
CSB
V
TH
V
REF0
V
REF1
V
REF2
V
REF3
V
REF4
V
REF5
V
REF6
000
1
1
0
0
1
VREF5
VTH < VREF
‘1’
VTH < VREF
‘0’

## Slide 31: Basic Operation: Page Read - MLC
Sensing the current through BLs
BL0
BL1
BL2
BL3
BL132,095
WLk
…
111
000
101
001
110
# of cells
111
E
110
P1
100
P2
000
P3
010
P4
011
P5
001
P6
101
P7
MSB
LSB
CSB
V
TH
V
REF0
V
REF1
V
REF2
V
REF3
V
REF4
V
REF5
V
REF6
1
1
0
0
1
VREF5
1
1
0
0
1
VREF3
VTH < VREF
‘1’
VTH < VREF
‘0’

## Slide 32: Basic Operation: Page Read - MLC
Sensing the current through BLs
BL0
BL1
BL2
BL3
BL132,095
WLk
…
111
000
101
001
110
# of cells
111
E
110
P1
100
P2
000
P3
010
P4
011
P5
001
P6
101
P7
MSB
LSB
CSB
V
TH
V
REF0
V
REF1
V
REF2
V
REF3
V
REF4
V
REF5
V
REF6
1
1
0
0
1
VREF5
1
1
0
0
1
VREF3
1
0
0
0
1
VREF1
1
0
0
0
1
XOR
VTH < VREF
‘1’
VTH < VREF
‘0’

## Slide 33: Basic Operation: Page Read – Takeaways
Bit-encoding affects the read latency!
  Compare # of sensing for LSB
# of cells
111
E
110
P1
100
P2
000
P3
010
P4
011
P5
001
P6
101
P7
MSB
LSB
CSB
V
TH
V
REF0
V
REF1
V
REF2
V
REF3
V
REF4
V
REF5
V
REF6
# of cells
111
E
110
P1
100
P2
101
P3
001
P4
000
P5
010
P6
011
P7
MSB
LSB
CSB
V
TH
V
REF0
V
REF1
V
REF2
V
REF3
V
REF4
V
REF5
V
REF6

## Slide 34: Basic Operation: Page Read – Takeaways
Bit-encoding affects the read latency!
  Compare # of sensing for LSB
# of cells
111
E
110
P1
100
P2
000
P3
010
P4
011
P5
001
P6
101
P7
MSB
LSB
CSB
V
TH
V
REF0
V
REF1
V
REF2
V
REF3
V
REF4
V
REF5
V
REF6
# of cells
111
E
110
P1
100
P2
101
P3
001
P4
000
P5
010
P6
011
P7
MSB
LSB
CSB
V
TH
V
REF0
V
REF1
V
REF2
V
REF3
V
REF4
V
REF5
V
REF6

## Slide 35: Basic Operation: Page Read – Takeaways
Bit-encoding affects the read latency!
  Compare # of sensing for LSB
# of cells
111
E
110
P1
100
P2
000
P3
010
P4
011
P5
001
P6
101
P7
MSB
LSB
CSB
V
TH
V
REF0
V
REF1
V
REF2
V
REF3
V
REF4
V
REF5
V
REF6
# of cells
111
E
110
P1
100
P2
101
P3
001
P4
000
P5
010
P6
011
P7
MSB
LSB
CSB
V
TH
V
REF0
V
REF1
V
REF2
V
REF3
V
REF4
V
REF5
V
REF6

## Slide 36: Basic Operation: Page Read – Takeaways
Bit-encoding affects the read latency!
  Compare # of sensing for LSB
# of cells
111
E
110
P1
100
P2
000
P3
010
P4
011
P5
001
P6
101
P7
MSB
LSB
CSB
V
TH
V
REF0
V
REF1
V
REF2
V
REF3
V
REF4
V
REF5
V
REF6
# of cells
111
E
110
P1
100
P2
101
P3
001
P4
000
P5
010
P6
011
P7
MSB
LSB
CSB
V
TH
V
REF0
V
REF1
V
REF2
V
REF3
V
REF4
V
REF5
V
REF6

## Slide 37: Today’s Agenda
NAND Flash Page Read/Write
Sensing Circuitry

## Slide 38: Read Mechanism
NAND flash read mechanism consists of three steps:
  1) Precharge
  2) Evaluation
  3) Discharge
P Precharge
⋯
V
PRE
Latch
OFF
⋯
V
PASS
Target WL
V
REF
C
SO
SO
BL
String
NAND
≤
V
TH
V
REF
a
>
V
TH
V
REF
b
M
PRE
D Discharge
❹
E Evaluation
⋯
V
PRE
Latch
ON
V
PASS
V
REF
⋯
⋯
V
PRE
Latch
OFF
0
0
⋯
BL
BL

## Slide 39: Read Mechanism: Precharge
P Precharge
⋯
V
PRE
Latch
OFF
⋯
V
PASS
Target WL
V
REF
C
SO
SO
BL
String
NAND
≤
V
TH
V
REF
a
>
V
TH
V
REF
b
M
PRE
D Discharge
❹
E Evaluation
⋯
V
PRE
Latch
ON
V
PASS
V
REF
⋯
⋯
V
PRE
Latch
OFF
0
0
⋯
BL
BL
Enable precharge transistor MPRE to charge all target BLs and their sense-out capacitors (CSO) to VPRE

## Slide 40: Read Mechanism: Evaluation
❹
E Evaluation
⋯
V
PRE
Latch
ON
V
PASS
V
REF
⋯
BL
D Discharge
P Precharge
⋯
V
PRE
Latch
OFF
⋯
V
PASS
Target WL
V
REF
C
SO
SO
BL
String
NAND
≤
V
TH
V
REF
a
>
V
TH
V
REF
b
M
PRE
⋯
V
PRE
Latch
OFF
0
0
⋯
BL
Target WL
≤
V
TH
V
REF

## Slide 41: Read Mechanism: Evaluation
Disconnect the BLs from VPRE and enable the latching circuit
❹
E Evaluation
⋯
V
PRE
Latch
ON
V
PASS
V
REF
⋯
BL
D Discharge
P Precharge
⋯
V
PRE
Latch
OFF
⋯
V
PASS
Target WL
V
REF
C
SO
SO
BL
String
NAND
≤
V
TH
V
REF
a
>
V
TH
V
REF
b
M
PRE
⋯
V
PRE
Latch
OFF
0
0
⋯
BL
Target WL
≤
V
TH
V
REF

## Slide 42: Read Mechanism: Evaluation
If VTH ≤ VREF , the charge in CSO quickly flows through the NAND string (Sensed as 1)
❹
E Evaluation
⋯
V
PRE
Latch
ON
V
PASS
V
REF
⋯
BL
D Discharge
P Precharge
⋯
V
PRE
Latch
OFF
⋯
V
PASS
Target WL
V
REF
C
SO
SO
BL
String
NAND
≤
V
TH
V
REF
a
>
V
TH
V
REF
b
M
PRE
⋯
V
PRE
Latch
OFF
0
0
⋯
BL
Target WL
≤
V
TH
V
REF

## Slide 43: Read Mechanism: Evaluation
❹
E Evaluation
⋯
V
PRE
Latch
ON
V
PASS
V
REF
⋯
BL
D Discharge
P Precharge
⋯
V
PRE
Latch
OFF
⋯
V
PASS
Target WL
V
REF
C
SO
SO
BL
String
NAND
≤
V
TH
V
REF
a
>
V
TH
V
REF
b
M
PRE
⋯
V
PRE
Latch
OFF
0
0
⋯
BL
Target WL
>
V
TH
V
REF
If VTH > VREF , the target cell blocks the BL discharge current (Sensed as 0)

## Slide 44: Read Mechanism: Discharge
Bitlines are discharged to return the NAND string to its initial state for future operations
D Discharge
⋯
V
PRE
Latch
OFF
0
0
⋯
BL
❹
E Evaluation
⋯
V
PRE
Latch
ON
V
PASS
V
REF
⋯
BL
P Precharge
⋯
V
PRE
Latch
OFF
⋯
V
PASS
Target WL
V
REF
C
SO
SO
BL
String
NAND
≤
V
TH
V
REF
a
>
V
TH
V
REF
b
M
PRE

## Slide 45: Latching Circuit
Before the evaluation step, the chip initializes the latching circuit
  Activating transistor

## Slide 46: Latching Circuit
The evaluation step
  Disables and
  Enables

## Slide 47: Inverse Read
Performing an inverse read by simply changing the activation sequence of and
  The precharge step activates
  The evaluation step disables and activates

## Slide 48: Flash-Cosmos, MICRO’22
https://arxiv.org/abs/2209.05566.pdf

## Slide 49
Required Material
49
Yu Cai, Saugata Ghose, Erich F. Haratsch, Yixin Luo, and Onur Mutlu, “Errors in Flash-Memory-Based Solid-State Drives: Analysis, Mitigation, and Recovery,” Invited Book Chapter in Inside Solid State Drives, 2018 - Introduction and Section 1
Jisung Park, Myungsuk Kim, Myoungjun Chun, Lois Orosa, Jihong Kim, and Onur Mutlu, “Reducing Solid-State Drive Read Latency by Optimizing Read-Retry,” In ASPLOS, 2021

## Slide 50
Recommended Material
50
Arash Tavakkol, Mohammad Sadrosadati, Saugata Ghose, Jeremie Kim, Yixin Luo, Yaohua Wang, Nika Mansouri Ghiasi, Lois Orosa, Juan Gómez Luna, and Onur Mutlu, “FLIN: Enabling Fairness and Enhancing Performance in Modern NVMe Solid State Drives,” In ISCA, 2018

## Slide 51: P&S Modern SSDs NAND Flash Read/Write Operations
Dr. Mohammad Sadrosadati
Prof. Onur Mutlu
ETH Zürich
Fall 2022
19 October 2022